## Slide 1: Eventtimer 10:00
Beamer HDMI 1 (PPP view)
Audio Mix Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Start Backup Recorder
Slidershow + Countdowntimer until eventtime reached or Pause if time < current time
T
JokiAutomation.exe "Timer" "10:00"

## Slide 2: Eventtimer Pause Text 1 Text 2
Beamer HDMI 1 (PPP view)
Audio Mix Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Slidershow + Pause, Text 1 and Text 2
P
JokiAutomation.exe "Pause" "Text 1" "Text 2"

## Slide 3: Band
Beamer HDMI 1 (PPP view)
Audio Mix Profile ‚Band‘
HDMI Switch channel 1 (Laptop PPP)
L
JokiAutomation.exe "Band"

## Slide 4: GoPro Actioncamera
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 2 (GoPro)
G
JokiAutomation.exe "GoPro"

## Slide 5: Camcorder 1 (cam with position controller)
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 3 (camcorder with position control)
A
JokiAutomation.exe "Altar"

## Slide 6: Prayer (prayer multi view)
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 5 (combination laptop and GoPro)
Beamer HDMI 1
MP
JokiAutomation.exe "Gebet"

## Slide 7: Readers (readers multi view)
Audio Mix Profile ‚Predigt‘
HDMI Switch channel 5 (combination laptop and GoPro)
Beamer HDMI 1
MR
JokiAutomation.exe "LesungMulti"

## Slide 8: Song (song multi view)
Audio Mix Profile ‚Band‘
HDMI Switch channel 5 (combination laptop and GoPro)
Beamer HDMI 1
MS
JokiAutomation.exe "BandMulti"

## Slide 9: Camcorder 2 (preacher view)
Audio Mix Profile ‚Predigt‘
HDMI Switch channel 4 (camcorder 2 preacher view)
K
JokiAutomation.exe "Predigt"

## Slide 10: Beamer Live Video View
Audio Mix Profile ‚VideoClip ‘
Switch beamer to HDMI 1 (Laptop view)
HDMI Switch channel 1 (Laptop )
BP
JokiAutomation.exe "BEAMER_LiveVideo"

## Slide 11: Beamer Livestream - View
Switch beamer to HDMI 2 (Livestream - view)
BS
JokiAutomation.exe "BEAMER_LiveStream"

## Slide 12: Beamer Videoclip Text 1 Text 2
Beamer analog input
Audio Mix Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Pause, Text 1 and Text 2
BA
JokiAutomation.exe "BEAMER_VideoClip" "Urheberrechtlich keine Liveübertragung" "Es geht in Kürze weiter"

## Slide 13: Beamer Mute / Demute
mutes / demutes the Beamer
BM
JokiAutomation.exe "BEAMER_Mute"

## Slide 14: Backup – Recorder Stop
stopps the backup recorder
RS
JokiAutomation.exe "Backup_Stop"

## Slide 15: shut down sequence
Stop Backup Recorder
Switch off Beamer
Switch off HDMI switch
Switch off backup recorder
Shut down raspberry pi
Ausschaltsequenz!!!
JokiAutomation.exe "Ausschaltsequenz"