## Slide 1: Eventtimer 10:00
Beamer HDMI 1 (PPP view)
Audio Mix Reset and then switched to Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Start Backup Recorder
Slidershow + Countdowntimer until eventtime reached or Pause if time < current time
T
JokiAutomation.exe "Timer" "10:00"

## Slide 2: Eventtimer Pause Text 1 Text 2
Beamer HDMI 1 (PPP view)
Audio Mix Reset and then switched to Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Slidershow + Pause, Text 1 and Text 2
P
JokiAutomation.exe "Pause" "Text 1" "Text 2"

## Slide 3: Band
Audio Mix Profile ‚Band‘
HDMI Switch channel 1 (Laptop PPP)
L
JokiAutomation.exe "Band"

## Slide 4: Text
Audio Mix Profile ‚Text‘
HDMI Switch channel 1 (Laptop PPP)
T
JokiAutomation.exe "Text"

## Slide 5: GoPro Actioncamera
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 2 (GoPro)
G
JokiAutomation.exe "GoPro"

## Slide 6: Camcorder 1 (cam with position controller)
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 3 (camcorder with position control)
A
JokiAutomation.exe "Altar"

## Slide 7: Prayer (prayer multi view)
Audio Mix Profile ‚Gottesdienst‘
HDMI Switch channel 5 (combination laptop and GoPro)
MP
JokiAutomation.exe "Gebet"

## Slide 8: Readers (readers multi view)
Audio Mix Profile ‚Predigt‘
HDMI Switch channel 5 (combination laptop and GoPro)
MR
JokiAutomation.exe "LesungMulti"

## Slide 9: Song (song multi view)
Audio Mix Profile ‚Band‘
HDMI Switch channel 5 (combination laptop and GoPro)
MS
JokiAutomation.exe "BandMulti"

## Slide 10: Camcorder 2 (preacher view)
Audio Mix Profile ‚Predigt‘
HDMI Switch channel 4 (camcorder 2 preacher view)
K
JokiAutomation.exe "Predigt"

## Slide 11: Live Video View
Audio Mix Profile ‚VideoClip ‘
HDMI Switch channel 1 (Laptop )
BP
JokiAutomation.exe "BEAMER_LiveVideo"

## Slide 12: Beamer Livestream - View
Toggles beamer between HDMI 2 (Livestream - view) and HDMI 1 (Laptop -View)
BS
JokiAutomation.exe "BEAMER_LiveStream"

## Slide 13: Beamer Videoclip Text 1 Text 2
Beamer analog input
Audio Mix Profile ‚Diashow‘
HDMI Switch channel 1 (Laptop PPP)
Pause, Text 1 and Text 2
BA
JokiAutomation.exe "BEAMER_VideoClip" "Urheberrechtlich keine Liveübertragung" "Es geht in Kürze weiter"

## Slide 14: Beamer Mute / Demute
mutes / demutes the Beamer
BM
JokiAutomation.exe "BEAMER_Mute"

## Slide 15: Backup – Recorder Start
starts the backup recorder
only used for pre church check, the backup recorder starts with sequence Timer
RC
JokiAutomation.exe "Backup_Start"

## Slide 16: Backup – Recorder Stop
stopps the backup recorder
RS
JokiAutomation.exe "Backup_Stop"

## Slide 17: Raspberry Pi – Reset
kills all RasPiAutomation processes at Raspberry Pi
only used for pre church check
RR
JokiAutomation.exe "RasPi_Reset"

## Slide 18: shut down sequence
Stop Backup Recorder
Switch off Beamer
Switch off HDMI switch
Switch off backup recorder
Shut down raspberry pi
Ausschaltsequenz!!!
JokiAutomation.exe "Ausschaltsequenz"

## Slide 19: Position Control Camcorder Move Sequence
moves camcorder 1 to position of param 2 (text of param 2 must be equal to teach position text of JoKi Automation listbox) after movement the view switches to camcorder 1.
Switches view during movement depending first uppercase letter of param 3 (A camcorder 1, G gopro action cam, K camcorder 2, L laptop)
Switches audio profile depending on second uppercase letter of param 3 (D laptop audio, G Gottesdienst, P Predigt, T Text, B Band)
Move Sequences should be combined with Raspberry Pi Reset sequence because timeout if move is not possible appears after one minute. The sequence can be interrupted by Raspberry Pi Reset before timeout appers.
This example moves camcorder 1 to positioon Taufstein with camcorder 2 view during movement and sound profile Predigt
JokiAutomation.exe "PositionControl" "Taufstein" "KP"
move
Reset RasPi

## Slide 20: Position Control Camcorder Move Sequence
moves camcorder 1 to position of param 2 (text of param 2 must be equal to teach position text of JoKi Automation listbox) after movement the view switches to camcorder 1.
Switches view during movement depending first uppercase letter of param 3 (A camcorder 1, G gopro action cam, K camcorder 2, L laptop)
Switches audio profile depending on second uppercase letter of param 3 (D laptop audio, G Gottesdienst, P Predigt, T Text, B Band)
Move Sequences should be combined with Raspberry Pi Reset sequence because timeout if move is not possible appears after one minute. The sequence can be interrupted by Raspberry Pi Reset before timeout appers.
This example moves camcorder 1 to positioon Mittelgang with GoPro view during movement and sound profile Band
JokiAutomation.exe "PositionControl" "Mittelgang" "GB"
move
Reset RasPi

## Slide 21: Position Control Camcorder Move Sequence
moves camcorder 1 to position of param 2 (text of param 2 must be equal to teach position text of JoKi Automation listbox) after movement the view switches to camcorder 1.
Switches view during movement depending first uppercase letter of param 3 (A camcorder 1, G gopro action cam, K camcorder 2, L laptop)
Switches audio profile depending on second uppercase letter of param 3 (D laptop audio, G Gottesdienst, P Predigt, T Text, B Band)
Move Sequences should be combined with Raspberry Pi Reset sequence because timeout if move is not possible appears after one minute. The sequence can be interrupted by Raspberry Pi Reset before timeout appers.
This example moves camcorder 1 to positioon Kanzel with Camcorder 1 view during movement and sound profile Text
JokiAutomation.exe "PositionControl" "Kanzel" "AT"
move
Reset RasPi